## Slide 1: Health and Safety Updates
Tanis Cooper Health and Safety Advisor

## Slide 2: OHSA Updates
Mandatory AEDs on Certain Construction Projects
Ontario now requires Automated External Defibrillators (AEDs) on many construction sites under the OHSA. Effective date January 1st, 2026
Applies to Construction projects:
20 or more workers, and projects expected to last 3 months or longer
Requirements: AED must be installed, accessible, and maintained on site
Required signage for AED location
Inspection, maintenance, and record‑keeping required
At least one worker trained in CPR/AED use must be present while work is underway
Washroom Facilities:
  A washroom cleaning log must be posted either (1) in a conspicuous place by the washroom facility; or (2) electronically, where it can be accessed by workers. Effective date January 1st, 2026

## Slide 3: Workplace Violence PREVENTION POLICY
Workplace Violence Harassment and Discrimination Policy revisions. Two separate policies now exist.
Violence Prevention Policy: for violent incidents or threats of violence.
Respect Policy and Conflict Resolution Process: for incidents of harassment and discrimination.
Notes: CGS has a Zero Tolerance Workplace Violence, Discrimination and Harassment Policy and Program in place.
Now have TWO separate policies that will account for all circumstances.
See "Respect Policy and Conflict Resolution Process" for incidents of harassment and discrimination
See the “Workplace Violence Prevention Policy” for violent incidents or threats.
Violence is defined as:
Use or attempted use of physical force
Statement or action threatening harm
Bringing a weapon into the workplace
Domestic Violence
This policy applies to all groups that interact with CGS employees. This includes all
  employees, elected officials, volunteers, service recipients, clients, residents, members of the public, suppliers and service providers.
The Respect Policy and reporting procedures should be consulted regarding incidents of workplace harassment or discrimination.
CGS personnel are guided and encouraged to report all acts of violence, discrimination and harassment, regardless of their source. We expect that our contractors have a similar policy in place and that it is enforced.
Necessary actions will be taken to protect our Employees and the public from acts of harassment and violence, and we will remove workers from sites when and if required.

## Slide 4: 2026 MLITSD Blitz
Building Opportunities in the Skilled Trades Act, 2021 (BOSTA) BOSTA:
Enforcing compliance with BOSTA, including authorization to work in compulsory trades.
MLITSD inspectors may:
Enter workplaces without notice
Inspect documents and training records
Interview workers
Issue compliance orders, notices of contravention, or administrative penalties
They enforce rules on unauthorized work, apprenticeship compliance, and proper certification under BOSTA.
LOTO:
Develop written LOTO procedures for all equipment.
Train workers on identifying hazardous energy sources and performing lockout safely (authorized and affected workers).
Ensure machinery is fully de‑energized and isolated before work begins.
Use appropriate locks, tags, and devices to prevent accidental re‑energization.
Notes: BOSTA:
MLITSD BOSTA enforcement ensures that only properly trained, certified, or registered individuals work in compulsory trades. Skilled Trades Ontario oversees certification and apprenticeship programs, while MLITSD focuses on compliance, inspections, and enforcement to keep Ontario’s skilled trades safe, regulated, and consistent.
What Lockout/Tagout Means
Lockout: Physically placing a lock on an energy‑isolating device to prevent equipment from starting. This includes electrical, mechanical, hydraulic, pneumatic, chemical, thermal, or other forms of hazardous energy.
Tagout: Attaching a tag that identifies who applied the lock, the date, and the reason for the lockout. Only the person who applied the lock and tag may remove them. [ccohs.ca]
Employer Requirements
Employers must:
Develop written LOTO procedures for all equipment.
Train workers on identifying hazardous energy sources and performing lockout safely (authorized and affected workers).
Ensure machinery is fully de‑energized and isolated before work begins.
Use appropriate locks, tags, and devices to prevent accidental re‑energization.
When LOTO Is Required
LOTO must be performed before any work involving:
Maintenance
Cleaning
Troubleshooting
Repair
Any task where a worker may be exposed to hazardous energy

## Slide 5: Hazard Reporting
OHSA section 28 – duty for Workers to report hazards
CGS staff will report hazards to Constructor’s Site Supervisor and document
Constructor is responsible to rectify hazards and provide safe environment
Notify visitors to site of hazards
Where a hazard remains unresolved – City to notify Ministry of Labour, Immigration, Training and Skills Development (MLITSD)
Notes: CGS staff who observe a hazard or contravention of the OHSA on a project will report the situation to the Constructor’s Site Supervisor and document the exchange.
The Constructor is responsible for all health and safety aspects of the project. The Constructor is responsible to ensure all visitors to site, including CGS Inspectors are made aware of the hazards they will encounter on site.
The Constructor is expected to mitigate hazards and rectify any concerns raised to reduce the risk of injury for all persons on the project. City Staff will not provide any instructions or direction on methods or procedures required to resolve the hazard or concern.
Where a hazard remains and has not been rectified by the Constructor or a contravention of the OHSA continues to exist, City Staff will notify the Ministry of Labour, Immigration, Training and Skills Development(MLITSD).

## Slide 6: Traffic Control/Book 7
OTM Book 7 signage and devices must be:
Compliant with Book 7 approved sign design patterns
Applied consistently according to standardized layouts, when modifying layouts, modifications must be documented
Maintained at high quality for visibility and safety. Must be replaced when no longer in good or moderate condition.
Installed/removed following Book 7 procedures
Employees must be trained in Book 7.
Notes: 1. Required Signage in Temporary Work Zones
Book 7 outlines mandatory sign design patterns, including shapes, colours, dimensions, and retroreflectivity levels for all temporary condition signs. These patterns are provided as official reference files for contractors.
Types of Signs
Regulatory: e.g., speed limits, lane control
Warning: e.g., workers ahead, lane shifts
Guide/Information: e.g., detour routes
Contractor Responsibilities
Use only approved Book 7‑compliant signs. Install signs at specified distances as shown in typical layouts. Ensure signs remain visible, upright, clean, and reflective.
2. Traffic Control Devices (TCDs)
OTM Book 7 covers specifications and quality guidelines for:
Cones & tubular markers
Barrels / drums
Barricades
Temporary delineators
Portable message signs (DMS)
Device Requirements
Must be high‑visibility and retroreflective
Must be kept in good physical condition
Must follow prescribed spacing and placement rules found in Book 7 layouts
3. Typical Work Zone Layouts
The Field Edition provides standardized layouts for:
Mobile operations
Intermittent work
Short‑ & long‑duration work
Freeway work zones
Layouts include:
Required signs and devices
Taper lengths & buffer zones
Worker and equipment positioning
Advanced warning areas and termination areas
Contractors must follow the layout that matches the work type and roadway conditions.
4. Traffic Control Persons (TCPs)
Book 7 includes specifications for:
TCP qualifications and training
TCP positioning and equipment
5. Setting Up and Removing Temporary Traffic Control
Contractors must follow Book 7’s prescribed procedures for:
Order of device installation (advance warning → transition → work area → termination)
Reverse‑order removal
Monitoring and adjusting devices to maintain safe conditions throughout the work

## Slide 7: Trench safety
Ontario trenching safety regulations require:
Proper soil assessment
Protective systems for trenches deeper than 1.2 m
Utility locates before digging
Safe access and fall prevention
Water and atmosphere control
Continuous monitoring and emergency planning
Notes: Key Requirements
1. Soil Assessment
Before digging, employers must:
Identify soil type as required under s. 226, since soil classification determines the protective system needed. Consider environmental factors (moisture, weather, vibration) that affect trench stability.
2. Protection Against Cave‑Ins
Trenches deeper than 1.2 m (4 ft) require a protective system unless walls are solid rock. Protective measures include:
Sloping or benching
Shoring systems
Trench boxes Engineered systems are required in specific circumstances under s. 235–242.
3. Locates and Service Identification
Before excavation:
All underground utilities (gas, electrical, water, sewer) must be located and marked as required under s. 228. Overhead power lines must also be identified (s. 188). Ensure proper permits are established with our utility companies when working around lines
4. Access, Egress, and Fall Protection
Employers must:
Provide safe entry and exit for workers.
Prevent falls into the excavation (s. 233(4)).
Ensure spoil piles and materials are kept away from trench edges (s. 232).
5. Water and Atmospheric Hazards
Must Remove accumulated water from excavations to prevent flooding and collapse (s. 230).
Evaluate for hazardous atmospheres such as toxic or flammable gases.
6. Worker Safety Practices
Workers must never enter a trench unless a second worker remains above ground (s. 225). Additional precautions include:
Proper PPE
Avoiding equipment‑related hazards
Maintaining good housekeeping
7. Emergency Preparedness
Employers must develop an emergency plan for trench rescues under s. 17–18.